## Slide 1: Quantum Sensing for the weather
Project Number: 24-1-1-3121.
Student names: Mohammad Shalabi.
Mentor name: Khen Cohen
Project location: The University.
Mentor signature:

## Slide 2: Project Topic
Quantum-Based Opportunistic Sensing for Weather Estimation
Goal: Extend classical weather monitoring techniques, into the quantum domain for higher accuracy and robustness.
Motivation:
  Classical methods: - Commercial Microwave Links (CMLs) are cost-effective but lack precision. - Classical weather sensing: measures signal strength attenuation. - Weather radar are Highly accurate but expensive.
  Quantum systems: - Highly sensitive to environmental disturbances, and subtle changes. - Detects effects like turbulence & phase distortion that classical systems miss. - Potential to stabilize quantum communication channels.
Notes: Classical weather sensing: measures signal strength attenuation
Quantum sensing: allows tracking entanglement changes directly
Entanglement may respond faster to environmental changes than power

## Slide 3: Project Topic
Approach:
  Use quantum communication protocols and opportunistic sensing to estimate weather conditions.
  Develop models to adapt quantum signals for resilience in adverse environments.
Research Questions:
  How do different noise models affect quantum signals?
  Can we determine environmental conditions from quantum state degradation?
  Are graph states more resilient or sensitive to noise than entangled photon pairs?

## Slide 4: Updated Project Scope & Methodology
Project Adjustments:
Plan change: From simulations + experiments to simulation-first .
If results are promising and time allows, the project may expand to include experiments.
Simulation Approach:
Initial Studies & Literature Review
  Simulated two entangled photons under simple noise profiles.
  Found that maximally entangled photon pairs experience only minor attenuation in entanglement.
Shift to Graph States
  Graph states provide a more complex and structured quantum system.
  Potentially more affected; ongoing study of entanglement degradation.
Noise Modeling
Notes: Start with a toy noise model: - Introduced Pauli noise, where a Pauli operator (X, Y, or Z) is applied with probability P. - N random Pauli operators are applied to the graph state. - Density matrix is analyzed to observe entanglement degradation.
If significant changes are observed in the density matrix and entanglement properties: - Move on to introducing physically accurate noise models. - Use log-normal and exponential noise distributions to simulate real weather conditions (rain, turbulence, dust storms).

## Slide 5: Updated Project Requirements
Simulation:
Concurrence Sensitivity: Track entanglement changes due to noise, ensuring 80% consistency in trends across simulations.
Frobenius & Fidelity Metrics: Maintain at least 85% correlation between Frobenius similarity and fidelity across noise levels.
Weather Condition Classification: Develop a method to classify weather conditions from graph state changes with atlest 75% accuracy.

## Slide 6: Updated Project Requirements
Experiment (if we end up doing one): - Simulation Validation: Ensure 80% similarity between experimental results and simulations. - Accuracy: Achieve at least a 5% improvement in signal accuracy compared to classical methods like CMLs. - Data Rate Requirement: Collect at least 100 measurements per second for detailed analysis

## Slide 7: Project Deliverables
Characterize entanglement degradation in graph states under Pauli noise - -- Explore how entanglement degrades with increasing P (probability) and N (number of operators). -Identify significant changes in quantum properties.
Expectation Value Calculations
  Focus on a single value of N at a time to analyze trends.
  Determine whether noise causes statistically significant changes in similarity.
Analysis of Results & Conclusion
  If Pauli noise shows clear effects, consider applying realistic noise models.
  Draw conclusions on the feasibility of quantum sensing in free-space channels.
4. Simulating weather condition-based noise and study their effects.
5. Experiment setup(maybe).

## Slide 8: Updated Block Diagram
In the blue box is the possible experiment workflow
Using the Qiskit library in python to create the qubits and the entanglements
Applying Pauli Operators - Done
Comparison between the density matrices - Done
Introducing a PDF that simulates actual weather disturbances, also in python – Next Steps
Measure the changes in the entanglement between the qubits

## Slide 9: Updated Block Diagram
Key Phases:
  Literature Review: Study classical and quantum sensing methodologies, focusing on environmental effects.
  Simulations: Model the impact of rain and turbulence on quantum channels.
  Experimental Setup (If time and resources permit):
    Construct a system and measure quantum signal behavior under different weather conditions.
  Data Analysis & Model Development:
    Compare classical attenuation models with quantum measurements.
    Develop new models based on experimental results.
  Validation: Compare simulation results with experimental data for accuracy assessment.

## Slide 10: Block Diagram of the current Simulation

## Slide 11: Project Products Achieved So Far
Initial Findings:
  Simple entangled pairs show minimal degradation under basic noise.
  Graph states display more sensitivity to noise.
Simulations Conducted:
  Generated and visualized graph states.
  Applied Pauli noise, analyzed fidelity and Frobenius similarity.
Next steps:
  Introduce realistic noise models.
  Evaluate how entanglement degradation correlates with physical conditions.

## Slide 12: Simulating and Visualizing Graph states
Notes: Just a Random graph state, with random entanglement values between states

## Slide 13: Toy Model Results

## Slide 14: Simulation Results - Fidelity & Frobenius Similarity
Graph state under Pauli noise:
  Fidelity decreases with increasing noise probability.
  Frobenius similarity provides additional insights into state changes.
Key Observations:
  Even a single Pauli operator can significantly alter the quantum state.
  Important for determining whether environmental effects can be detected.
  Changing the probability linearly, showed a linear change in the expected value, which might indicate that it would behave similarly with a given probability distribution, in turn we’d be able to identify the noise/ weather profile.

## Slide 15: Updated Project Schedule
 | Milestone | Planned Date | Actual Delivery date | Remarks
1. | Literature Review | Mid-to-late November 2024 |  | It’s a research project, so the learning is always ongoing
2. | Experimental Design | Early December 2024 |  | Didn’t happen, got started with the simulations instead!
3. | Initial data collection | Mid to Late December 2024 |  | If time and resources permit
4. | Simulation Framework Setup | Early January 2025 | Mid December 2024 | Since the generator wasn’t available, we had to start with the simulations, also the switch to graph states, made us redo the simulation a few time, since we came up with a new idea of how to do things every other week
5. | Simulation Phase I | Mid to Late January 2025 | Late January 2024 | 
6. | Progress Presentation Submission | 2.2.2025-9.3.2025 | Happening right now! | 
7. | Simulation Phase II | Mid to Late March 2025 | Mid to Late March 2025 | Introduce more physically accurate noise distributions
8. | Experiment Setup Completion | Early April 2025 |  | If time and resources permit
9. | Data Collection Begins | Mid-April 2025 |  | 
11. | Data Analysis Phase I | Early to Mid-May 2025 |  | 
10. | Poster Submission and finishing the work | 25.5.2025 |  | 
12. | Final Data Analysis | Early to Mid-June 2025 |  | 
13. | Final Deliverables Preparation | Late June 2025 |  | 
14. | Final deliverables submission | July– August 2025 |  |